## Slide 1
Smarter Doorbell: Edge Computing Resolution
based on ESP32-S3 and Edge Impulse

## Slide 2
QUAN
SUN (my cat)
Team members
1. Cause Troubles
2. Provide training data
1. 🛠️ Hardware & Environment Setup
2. 🧠 tinyML Model Development
3. 💻 Edge Deployment & Integration
4. ✅ Testing & Finalization

## Slide 3
High Performance: Achieved 30+ FPS for real-time face detection using standard OpenCV libraries.
Ease of Development: Python environment allowed for rapid iteration and testing of complex models.
Results: Raspberry Pi 5 Based Smart Doorbell
Successful Recognition: In real environment test, it successfully recognized me, my cat and strangers.

## Slide 4
Power & Heat
The Pi 5 is power-hungry, requiring a 5V/3A+ active supply. It cannot run on standard batteries for long, making wireless installation impossible. Active cooling is also required to prevent throttling.
High Cost
At ~$100, the unit cost is prohibitive for a scalable IoT product. Additionally, the full Linux OS boot time (20-30s) prevents "instant-on" capture when a visitor presses the button.
Bottlenecks: The Pi 5 Approach
Large Size
The whole device size could be 100x100x65 mm since it have the extension board of the ink screen, m2 ssd, cooling fan and batteries
To be Hacked
It can be hacked because the whole system was running on the linux system and we exposed the interfaces of HDMI and usb.

## Slide 5
Energy Efficient
Microcontrollers consume milliwatts, allowing for months of operation on a single battery charge.
Low Latency
Local inference on the ESP32 eliminates the round-trip time to the cloud, providing instant alerts.
Privacy
Images are processed on-device. No video stream is sent to the cloud, ensuring total user privacy.
The Advantages of TinyML on ESP32S3

## Slide 6
Data Ingestion
Collecting dataset of known faces.
Create Impulse for model Training
Edge Impulse Pipeline
DSP
Image preprocessing & resizing.
Impulse

## Slide 7
Training
Transfer learning (MobileNetV2).
Validation
Testing model accuracy vs F1 score.
Deployment
Export as Arduino/C++ library.
Edge Impulse Pipeline

## Slide 8
System Schematic
When the PIR sensor detects movement, it wakes up the ESP32-S3. The camera captures an image and processes it, then a TinyML model performs face detection and recognition. The system decides whether the face is known and sends the appropriate event to Home Assistant via MQTT. After logging and notifications, the ESP32-S3 enters deep-sleep mode to save power.

## Slide 9
Core Components
MCU: Seeed Xiao ESP32-S3 Sense
Sensor: Seeed Grove - Digital PIR Sensor
Power: 400mAh 3.7V Li-Po Battery
Housing: Custom 3D Printed PLA Enclosure.
Hardware Stack
Camera: OV2640 2MP Camera Module.
Dimensions: 24x55x17 mm
Cost: 13+4+2+1 = 20 USD

## Slide 10
Real Environment Testing
The system was deployed in a real-world scenario to validate reliability.
Conditions: Tested in varying lighting conditions (direct sunlight vs porch shade). The model successfully identified residents while ignoring non-human motion triggers.
380mA Work Mode
83uA Sleep Mode
400mAh battery can work for 32 days, based on the assumption of 10 sec per detection, 10 times detection a day

## Slide 11
The doorbell communicates with Home Assistant via the MQTT protocol over Wi-Fi.
Triggers: Doorbell camera sends an instant notification to mobile devices.
Automation: "Person Detected" event triggers porch lights to turn on automatically.
Dashboard: Displays last captured image and battery status.
Home Assistant Insertion
See my another github: https://github.com/Zachay-NAU/ESPHome-Support-on-Seeed-Studio-XIAO-ESP32S3